Inch Size Model R L H W Wt (lbs.) Avanti .7 .92 2.93 4.20 1.78 2.4 Avanti 1 1.14 4.71 4.70 2.17 3.30 Avanti 3 1.50 6.14 6.12 2.90 7.10 Avanti 5 1.80 7.36 7.10 3.38 9.80 Avanti 8 1.88 7.91 7.65 3.90 13.70 Avanti 10 2.13 9.20 8.90 4.35 20.90 Avanti 20 2.50 10.84 9.90 5.00 35.20 Avanti 35 3.01 13.06 11.93 6.02 67.20 Avanti 50 3.39 14.71 13.44 6.79 87.50 Metric Size Model R L H W Wt (kg.) Avanti.7 23.4 74.4 107 45 1.08 Avanti 1 29 119.6 119.4 55.1 1.49 Avanti 3 38.1 156 155.5 73.7 3.20 Avanti 5 45.7 186.9 180.3 85.9 4.41 Avanti 8 47.8 200.9 194.3 99.1 5.17 Avanti 10 54.1 233.7 226.1 110.5 9.41 Avanti 20 63.5 275.3 251.5 127 15.84 Avanti 35 76.5 331.7 303 152.9 30.24 Avanti 50 86.1 373.6 341.4 172.5 39.38 Torque Specifications Inch Size Model AO AR S Sq Avanti .7 2.4 5.76 .47 .75 Avanti 1 2.38 6.09 .50 .75 Avanti 3 3.17 8.12 .75 1.00 Avanti 5 3.83 9.72 .80 1.50 Avanti 8 4.58 10.23 .88 1.50 Avanti 10 4.58 12.15 1.00 1.50 Avanti 20 5.75 14.58 1.20 2.50 Avanti 35 6.93 17.57 1.45 2.50 Avanti 50 7.80 19.79 1.63 2.50

| International Design Patent Applied and Received |  | HYTORC invented the co-axial reaction/drive system, eliminating over 70% of all Hydraulic Torque Tool failure resulting from internal torsion created between the reaction arm on one end and the drive on the other end of the tool. Tool placement is improved to 360 degree around the nut. Reaction Arms won't pull off during operation and tool handling is simplified with the new Simul-Torc Switch. 360 degree Job-adjustable Super Alloy 360 x 240 degree Uni-swivel Torsion-free internal Mechanism Upgradeable for Stretch-to-load! View Avanti Specific Data Dimensions Operations Manual (pdf) Torque Charts Parts List (pdf) | Award-winning Super Light-weight Anti Backlash Pawl Corrosion-resistant Simultorc-switch* New Ergonomic Design |
| --- | --- | --- | --- |
|  |  | HYTORC in pursuit of Perfection! |

Avanti Pressure/Torque Conversion Chart

In Ft. Lbs

| Avanti | 3 |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Pressure in PSI | Torque in Ft. Lbs. |
| 1500 | 445 |  |  |  |  |  |  |  |  |
| 1600 | 476 |  |  |  |  |  |  |  |  |
| 1800 | 538 |  |  |  |  |  |  |  |  |
| 2000 | 600 |  |  |  |  |  |  |  |  |
| 2200 | 662 |  |  |  |  |  |  |  |  |
| 2400 | 725 |  |  |  |  |  |  |  |  |
| 2600 | 787 |  |  |  |  |  |  |  |  |
| 2800 | 850 |  |  |  |  |  |  |  |  |
| 3000 | 912 |  |  |  |  |  |  |  |  |
| 3200 | 975 |  |  |  |  |  |  |  |  |
| 3400 | 1038 |  |  |  |  |  |  |  |  |
| 3600 | 1100 |  |  |  |  |  |  |  |  |
| 3800 | 1163 |  |  |  |  |  |  |  |  |
| 4000 | 1226 |  |  |  |  |  |  |  |  |
| 4200 | 1288 |  |  |  |  |  |  |  |  |
| 4400 | 1350 |  |  |  |  |  |  |  |  |
| 4600 | 1412 |  |  |  |  |  |  |  |  |
| 4800 | 1474 |  |  |  |  |  |  |  |  |
| 5000 | 1536 |  |  |  |  |  |  |  |  |
| 5200 | 1598 |  |  |  |  |  |  |  |  |
| 5400 | 1660 |  |  |  |  |  |  |  |  |
| 5600 | 1722 |  |  |  |  |  |  |  |  |
| 5800 | 1784 |  |  |  |  |  |  |  |  |
| 6000 | 1846 |  |  |  |  |  |  |  |  |
| 6200 | 1908 |  |  |  |  |  |  |  |  |
| 6400 | 1970 |  |  |  |  |  |  |  |  |
| 6600 | 2032 |  |  |  |  |  |  |  |  |
| 6800 | 2094 |  |  |  |  |  |  |  |  |
| 7000 | 2156 |  |  |  |  |  |  |  |  |
| 7200 | 2218 |  |  |  |  |  |  |  |  |
| 7400 | 2280 |  |  |  |  |  |  |  |  |
| 7600 | 2343 |  |  |  |  |  |  |  |  |
| 7800 | 2405 |  |  |  |  |  |  |  |  |
| 8000 | 2467 |  |  |  |  |  |  |  |  |
| 8200 | 2530 |  |  |  |  |  |  |  |  |
| 8400 | 2593 |  |  |  |  |  |  |  |  |
| 8600 | 2655 |  |  |  |  |  |  |  |  |
| 8800 | 2718 |  |  |  |  |  |  |  |  |
| 9000 | 2781 |  |  |  |  |  |  |  |  |
| 9200 | 2842 |  |  |  |  |  |  |  |  |
| 9400 | 2903 |  |  |  |  |  |  |  |  |
| 9600 | 2963 |  |  |  |  |  |  |  |  |
| 9800 | 3024 |  |  |  |  |  |  |  |  |
| 10000 | 3085 |  |  |  |  |  |  |  |  |

The AVANTI tool is the only hydraulic wrench with the reaction arm on the bottom of the wrench for added safety.